Introduction
Including libDuik in your scripts
Installing libDuik
Using libDuik
Modifying libDuik

Pseudo Effects List

Objects
KeySpatialProperties Object
KeyFrame Object
PropertyAnim Object
MaskAnim Object
EffectAnim Object
LayerAnim Object
IKRig Object

Duik Object
Attributes
Objects
Methods
IK
goal
addController
addControllers
wiggle
exposure
addBones
addZeros
rotationMorph
swing
wheel
morpher
lensFlare
distanceLink
spring
replaceInExpressions
replaceInLayersExpressions
copyAnim
pasteAnim

Duik.setup

Attributes
Methods
installPseudoEffects
checkPresetEffectsVersion

Duik.uiStrings

Attributes

Duik.settings
Attributes
Methods
save
load
restoreDefaults

Duik.utils
Methods
prepareProperty
getPropertyDimensions
getLength
getAverageSpeed
addPseudoEffect
getPuppetPins
getDistance
rigProperty
deselectLayers
checkNames
getItem
getKey
getPropertyAnims
getPropertyAnim
setPropertyAnim
addKey
getFirstKeyTime
hasSelectedKeys
convertCollectionToArray
prepIK
Introduction

libDuik is a complete library of objects, attributes and methods from Duik – Duduf IK & Animation Tools for After Effects. It allows to easily include Duik functions into other scripts.

Including libDuik in your scripts

There are three ways to use libDuik in your scripts:

• #include «libDuik.jsxinc»
Adding this line at the beginning of the script automatically loads libDuik at first run of the script. libDuik.jsxinc must be in the same folder as your script.
This is the recommended way of including libDuik.

• Copying all content of libDuik.jsxinc in the beginning of your script
Copying the whole library inside your script allows you to deploy only one file.

• Renaming libDuik.jsxinc to libDuik.jsx and move it to Scripts/Startup/
libDuik will be loaded during After Effects startup, and will then be available to all scripts. This is a good way to use Duik functions in severeal scripts without having to include libDuik in all scripts.

Installing libDuik

• Using pseudo effects
This is the default behaviour, and you should prefer to use libDuik this way.

At first launch, libDuik will automatically check if the pseudo effects it needs are already installed, and, if not, it will attempt to install them, by writing them in the file called presetEffects.xml inside the installation folder of After effects.
To achieve this, libDuik needs to be allowed to write files by After Effects. The only way to do this is for the user to check the box called « Allow scripts to write files... » in the general preferences of After Effects.

Note: You can open the preferences dialog in your scripts with:
app.executeCommand(2359);
but the user will have to check the box itself.

After the very first run of libDuik, if the pseudo effects were not already available, the user will have to restart After Effects for the pseudo effects to be loaded by After Effects.

If you want to use libDuik without allowing the scripts to write files, you can manually add the pseudo effects to presetEffects.xml: Copy/paste the content of the file Duik_presetEffects.xml distributed with libDuik, in presetEffects.xml, just before the last line « </effects> ».
Note that on Mac OS you will have to change the file permissions to be able to modify it.

• Using presets
If you cannot modify presetEffects.xml, or for any other reason, you can use .ffx presets.
You just have to set Duik.usePresets to true.

Note: if libDuik was not able to update presetEffects.xml, it will default Duik.usePresets to true. If presetEffects.xml is up-to-date, Duik.usePresets will be false by default.
By default, libDuik will look for .ffx files inside its own folder. You can specify another folder by setting the path to Duik.presetPath with an ending « / ».
The .ffx files must be named by the corresponding pseudo effects matchNames plus the extension (.ffx). A complete list of those matchNames is available in this document.

Note: if presetEffects.xml is not updated with libDuik pseudo effects, when using presets After Effects may warn for missing effects. libDuik will work well anyway.

Note: the presets distributed with libDuik are CC2014 versions (for this alpha version of libDuik. Later versions may be distributed with CS6, or even CS4 versions of presets). Sadly, After Effects presets cannot be used with older versions of After Effects than the one used to create them. If you need to use presets with older versions, you will have to create your own.

Using libDuik

Once libDuik has been loaded, all its classes, attributes and methods are available in the javascript object Duik, for all scripts run by After Effects.

libDuik is loaded only once; this allows a faster launch of your scripts.

Modifying libDuik

If you're modifying libDuik and need to test it without having to reboot After Effects to reload it, you can un-comment the first line:
if (typeof Duik === 'object') delete Duik;
inside libDuik itself, or you can include this line in your own script before #include libDuik;
Pseudo Effects List

libDuik uses pseudo effects instead of expression controls. Those effects must be added to presetEffects.xml (see Introduction, Installing libDuik for more details).
The XML code used to create those effects is Duik_presetEffects.xml

Here is a list of the effects available.

Those effects can be added on any layer with:
layer.effect.addProperty(matchName)
Example:
app.project.activeItem.layer(1).effect.addProperty('DUIK_One_Layer_IK');

matchName	Description	Screenshot
DUIK_One_Layer_IK	Used by one layer IK
DUIK_Two_Layer_IK	Used by two layer IK
DUIK_3D_Wiggle	Used for wiggle on 3D properties
DUIK_2D_Wiggle	Used by wiggle on 2D properties
DUIK_1D_Wiggle	Used by wiggle on 1D properties
DUIK_Exposure	Used by exposure, in fixed mode
DUIK_RotMorph	Used by Rotation Morph
DUIK_Swing	Used by Swing (oscillation)
DUIK_Wheel	Used by Wheel
DUIK_LensFlare	Used by Lens Flare on the layer of the center to control size and intensity
DUIK_LensFlareDistance	Used by Lens Flare on flare layers to control their distance from the center
DUIK_DistanceLink	Used by Distance Link
DUIK_Spring	Used by Spring on 2D and 3D properties
DUIK_Spring_Bounce	Used by spring on 1D properties, includes a checkbox called 'bounce'.

Objects

libDuik creates new javascript instantiable javascript objects, which can be very helpful when working with After Effects, and are needed by Duik.

Name	Description
KeySpatialProperties	Describes all spatial properties of a KeyFrame.
KeyFrame	Represents an animation keyframe of After Effects
PropertyAnim	Describes the keyframe animation of a given property
MaskAnim	Describes all the keyframe animations of the properties of a given Mask
EffectAnim	Describes all the keyframe animations of the properties of a given Effect
LayerAnim	Describes all the keyframe animations of the transformation, masks, and effects of a layer
IKRig	Describe an IK created by Duik (layers needed, type, goal, controller...)

KeySpatialProperties object attributes

Describes all spatial properties of a KeyFrame.

KeySpatialProperties.inTangent
KeySpatialProperties.outTangent
KeySpatialProperties.continuous
KeySpatialProperties.autoBezier
KeySpatialProperties.roving

Name	Type	Description
inTangent	float or Array of float	In spatial tangent of the keyframe
outTangent	float or Array of float	Out spatial tangent of the keyframe
continuous	boolean	Spatial interpolation set to continuous
autoBezier	boolean	Spatial interpolation set to auto Bezier
roving	boolean	Keyframe set to roving

KeyFrame object attributes

Represents an animation keyframe of After Effects
See Duik.utils.getKey() and Duik.utils.addKey()

KeyFrame.time
KeyFrame.value
KeyFrame.inInterpolationType
KeyFrame.outInterpolationType
KeyFrame.spatial
KeyFrame.spatialProperties
KeyFrame.inEase
KeyFrame.outEase
KeyFrame.continuous
KeyFrame.autoBezier

Name	Type	Description
time	float	Time of the keyframe in the comp
value	Any AFX propertyValueType	Value of the keyframe
inInterpolationType	Enumerated value; one of: KeyframeInterpolationType.LINEAR / KeyframeInterpolationType.BEZIER / KeyframeInterpolationType.HOLD	In interpolation type of the keyframe
outInterpolationType	Enumerated value; one of: KeyframeInterpolationType.LINEAR / KeyframeInterpolationType.BEZIER / KeyframeInterpolationType.HOLD	Out interpolation type of the keyframe
spatial	boolean	True if the keyframe is on a spatial property, one of: PropertyValueType.ThreeD_SPATIAL / PropertyValueType.TwoD_SPATIAL
spatialProperties	KeySpatialProperties	All spatial properties of the keyframe. See KeySpatialProperties object attributes
inEase	Array of AFX KeyframeEase objects	Incoming temporal ease of the keyframe
outEase	Array of AFX KeyframeEase objects	Outgoing temporal ease of the keyframe
continuous	boolean	Temporal interpolation set to continuous

PropertyAnim object attributes

Describes the keyframe animation of a given property
See Duik.utils.getPropertyAnim() and See Duik.utils.setPropertyAnim()

PropertyAnim.name
PropertyAnim.keys
PropertyAnim.startValue

Name	Type	Description
name	string	Name of the animated Property
keys	Array of KeyFrames	Keyframes of the animation, see KeyFrame object attributes
startValue	Any AFX propertyValueType	First value of the animation. If there's no keyframe PropertyAnim.keys.length == 0, the value of the property.

MaskAnim object attributes

Describes all the keyframe animations of the properties of a given Mask
See Duik.utils.getPropertyAnims()

MaskAnim.name
MaskAnim.anims

Name	Type	Description
name	string	Name of the animated Mask
anims	Array of PropertyAnim	Animations of the properties of the mask, see PropertyAnim object attributes

EffectAnim object attributes

Describes all the keyframe animations of the properties of a given Effect
See Duik.utils.getPropertyAnims()

EffectAnim.name
EffectAnim.matchName
EffectAnim.anims

Name	Type	Description
name	string	Name of the animated Effect
matchName	string	matchName of the animated Effect
anims	Array of PropertyAnim	Animations of the properties of the effect, see PropertyAnim object attributes

LayerAnim object attributes

Describes all the keyframe animations of the transformation, masks, and effects of a layer
See Duik.copyAnim() and Duik.pasteAnim()

LayerAnim.name
LayerAnim.index
LayerAnim.transformAnims
LayerAnim.effectsAnims
LayerAnim.masksAnims

Name	Type	Description
name	string	Name of the animated layer
index	string	Index of the animated layer
transformAnims	Array of PropertyAnim	Animations of the transformations, see PropertyAnim object attributes
effectsAnims	Array of EffectAnim	Animations of the effects, see EffectAnim object attributes
masksAnims	Array of MaskAnim	Animations of the masks, see MaskAnim object attributes

IKRig object attributes

Describe an IK created by Duik.

IKRig.type
IKRig.layer1
IKRig.layer2
IKRig.layer3
IKRig.goal
IKRig.controller

Name	Type	Description
type	int	Type of the IK, either 1, 2, or 3. 0 if the IK is not valid.
layer1	AVLayer	First layer of the IK (the root, the top parent)
layer2	AVLayer or null	The second layer of the IK, if type is 2 or 3, or null if type is 1.
layer3	AVLayer or null	The third layer of the IK, if type is 3, or null if type is 1 or 2.
goal	AVLayer or null	A goal layer attached to the IK, or null
controller	AVLayer	The controller layer of the IK
threeD	boolean	true if this is a 3D IK (used for type 2 only)
frontFacing	boolean	true if the 3D layers face the front/back views, false if they face the right/left views.
clockWise	boolean	true if the IK bends clockwise. Used with type 2 and 3 only.
created	boolean	true if the IK has already been successfully created and exists in the comp.

IKRig object methods

IKRig.create()

Name	Description	Return
create()	Creates the rig in the comp	AVLayer, the zero created (if any) or null

IKRig.create()

Creates the IK Rig in the comp. Sets the created attribute to true if sucessful.

returns

AVLayer, the zero created (if any) or null.
Duik

Duik Attributes

string Duik.version
float Duik.versionNumber
boolean Duik.forceReload
boolean Duik.usePresets
string Duik.presetPath
float Duik.presetEffectsInstalledVersion

Name	Type	Description
version	string, read-only	Version string of libDuik
versionNumber	float, read-only	Version number of libDuik
usePresets	boolean	true to use presets instead of pseudo effects.
presetPath	string	Path where presets are located; By default, the path of libDuik.jsxinc itself.
presetEffectsInstalledVersion	float, read-only	Version number of installed pseudo effects. Should be the same of Duik.versionNumber
copiedAnim	Array of LayerAnim	The layer animations copied with Duik.copyAnim() method.

Duik Objects

Duik.uiString
Duik.settings
Duik.utils
Duik.setup

Name	Description
uiStrings	Contains all string names used by effects created by Duik. / You can set these strings to translate libDuik at runtime. / Default values are English names.
settings	Access to settings used by Duik.
utils	Some useful tools
setup	Methods and attributes to correctly install libDuik & pseudo effects.

Duik Methods

//TODO tri par ordre alphabétique

Low-level methods are listed below (greyed) but they are not documented.
If you do not understand what low-level methods do by reading them in libDuik.jsxinc, you shouldn't need them.

Duik.IK(controller, layer1, layer2, layer3, goal, clockWise, frontFacing)
Duik.goal(layer, controller)
Duik.addController(layer)
Duik.addControllers(layers)
Duik.oneLayerIK(controller,layer)
Duik.twoLayerIK(controller,root,end,clockWise,frontFacing)
Duik.wiggle(layer,property,separateDimensions)
Duik.threeDWiggle(layer,property,)
Duik.twoDWiggle(layer,property)
Duik.oneDWiggle(layer,property)
Duik.exposure(layer,property,adaptative,limit,minExp,maxExp)
Duik.adaptativeExposure(layer,property,precision,minExp,maxExp)
Duik.fixedExposure(layer,property)
Duik.addBones(layers)
Duik.addZeros(layers)
Duik.rotationMorph(layer,prop)
Duik.swing(layer,prop)
Duik.wheel(layer,radius,curved)
Duik.morpher(layers)
Duik.lensFlare(layers)
Duik.distanceLink(layer, property, parentLayer)
Duik.spring(property, layer, simulated)
Duik.utils.replaceInExpressions(prop,oldString,newString)
Duik.replaceInLayersExpressions(layers, oldString, newString)
Duik.copyAnim(layers, selectedKeysOnly, startTime, endTime)
Duik.pasteAnim(layers, layerAnims, startTime, useIndexes)

Name	Description	Return
IK(controller, layer1, layer2, layer3, goal, clockWise, frontFacing)	Adds IK on the layers	true if successful, false if anything went wrong
goal(layer, controller)	Adds a goal effect to the layer, which may be controlled by a controller	true if successful, false if anything went wrong
addController(layer)	Creates a null object (controller) at layer position and named by layer.name	AVLayer; controller
addControllers(layers)	For each layer, / Creates a null object (controller) at layer position and named by layer.name	Array of AVLayer; controllers
wiggle(layer, property, separateDimensions)	Adds a wiggle effect to given property	true if successful, false if anything went wrong
exposure(layer, property, adaptative, precision, minExp, maxExp)	Adds exposure controles to given property	true if successful, false if anything went wrong
addBones(layers)	Adds bones to the layers	Array of AVLayer; / bones
addZeros(layers)	Adds zeros to the layers	Array of AVLayer; / zeros
rotationMorph(layer, prop)	Creates a rotation morph on the given property	true if successful, false if anything went wrong
swing(layer,prop)	Creates a swing on the given property	true if successful, false if anything went wrong
wheel(layer, radius, curved)	Automates the rotation of the given layer using its position	true if successful, false if anything went wrong
morpher(layers)	Adds a slider to easily control interpolations of selected properties of the given layers.	true if successful, false if anything went wrong
lensFlare(layers)	Rigs the layers to move like a lens flare.	true if successful, false if anything went wrong
distanceLink(layer, property, parentLayer)	Links the property to the distance of parentLayer	true if successful, false if anything went wrong
spring(property, layer, simulated)	Adds a spring effect on the properties	true if successful, false if anything went wrong
replaceInLayersExpressions(layers, oldString, newString)	Replaces all occurences of oldString by newString in all the expressions of all the layers.	Void
copyAnim(layers, selectedKeysOnly, startTime, endTime)	Copies the animation of the layers	Array of LayerAnim
pasteAnim(layers, layerAnims, startTime, useIndexes)	Pastes the animations on the layers	int, the number of the layers on which an animtion was pasted

Duik.IK(controller, layer1, layer2, layer3, goal, clockWise, frontFacing)

Adds IK on the layers

parameters:

controller | AVLayer
layer1 | AVLayer
layer2 | AVLayer or undefined
layer3 | AVLayer or undefined
goal | AVLayer or undefined
clockWise | boolean, used only with two-layer and three-layer IK, default: false
frontFacing | boolean, default: false

returns

true if successful, false if anything went wrong

Duik.goal(layer, controller)

Adds a goal effect to the layer, which may be controlled by a controller

parameters:

layer	| AVLayer
controller | AVLayer or undefined

returns

true if successful, false if anything went wrong

Duik.addController(layer)

Creates a null object (controller) at layer position and named by layer.name

parameters

layer | AVLayer

returns

AVLayer controller

Duik.addControllers(layers)

This is a convenience method, which runs Duik.addController(layer) on each layer of the given array of layers.

parameters

layers | Array of AVLayer

returns

Array of AVLayer controllers

Duik.wiggle(layer, property, separateDimensions)

Adds a wiggle effect to given property.

parameters

layer | AVLayer of the property
property | Property
separateDimensions | boolean, false to apply the same wiggle to all dimensions, default: false

returns

true if successful, false if anything went wrong

Duik.exposure(layer, property, adaptative, limit, minExp, maxExp)

Adds exposure controls to given property.

parameters

layer | AVLayer of the property
property | Property
adaptative | boolean, default: true
limit | float, default: 100
minExp | integer, default : 1, minimum exposure
maxExp | integer, default : 4, maximum exposure

returns

true if successful, false if anything went wrong

Duik.addBones(layers)

Adds bones to the layers, only on selected pins if any, or else on all puppet pins found on those layers.

parameters

layers | Array of AVLayers

returns

Array of AVLayers, the bones created

Duik.addZeros(layers)

Adds a null object for each layer, at the same place and orientation, and then parents the layer to it, parenting the null object (the zero) to the former parent of the layer.

parameters

layers | Array of AVLayers

returns

Array of AVLayers, the zeros created

Duik.rotationMorph(layer,prop)

Creates a rotation morph on the given property.

Parameters

layer | AVLayer
prop | Property

returns

true if successful, false if anything went wrong

Duik.swing(layer,prop)

Creates a swing on the given property

parameters

layer | AVLayer
prop | Property

returns

true if successful, false if anything went wrong

Duik.wheel(layer, radius, curved)

Automates the rotation of the given layer using its position.
If curved, works even if the trajectory is not horizontal, but is heavier to compute.

parameters

layer | AVLayer
radius | float, default 100.0
curved | boolean, default false

returns

true if successful, false if anything went wrong

Duik.morpher(layers)

Adds a "morpher", a slider to easily control interpolations of selected properties of the given layers.

parameters

layers | Array of AVLayer

returns

true if successful, false if anything went wrong

Duik.lensFlare(layers);

Rigs the layers to move like a lens flare. The first layer in the selection is the controller, with sliders for intensity and size; the other layers have a distance property to adjust their position along the lens flare.

parameters

layers | Array of AVLayer

returns

true if successful, false if anything went wrong

Duik.distanceLink(layer,property,parentLayer);

Links the property to the distance of parentLayer

parameters

layer | AVLayer containing the property
property | Property to rig
parentLayer | AVLayer which distance from layer is used to rig

returns

true if successful, false if anything went wrong

Duik.spring(property, layer, simulated);

Adds a spring effect on the property

parameters

property | Property
layer | AVLayer containing the property
simulated | if true, applies the simulated version of the spring, default: false

returns

true if successful, false if anything went wrong

Duik.replaceInLayersExpressions(layers, oldString, newString)

Replaces all occurences of oldString by newString in all the expressions of all the layers.

parameters

layers | Array of AVLayers or LayerCollection
oldString | string
newString | string

returns

void

Duik.copyAnim(layers, selectedKeysOnly, startTime, endTime)

Copies all the animations as LayerAnim objects (except expressions) on selected layers, and store them in the Array Duik.copiedAnim.
If selectedKeysOnly is true, copies only the selected keyframes, otherwise all the masks, effcts, and transformation properties will be copied, even if they are not animated (in this case, the value will be stored in the PropertyAnim.startValue). If you do not want to keep the properties without animation, you will have to loop through the arrays of PropertyAnim and check if PropertyAnim.keys.length > 0 to remove empty animations from the Arrays.
See LayerAnim object

parameters

layers | Array or Collection of AVLayers
selectedKeysOnly | boolean, true to copy only selected keys, default: false
startTime | float, default: start of the comp
endTime | float, default: end of the comp

returns

Array of LayerAnim

Duik.pasteAnim(layers, layerAnims, startTime, useIndexes);

Pastes all the animations in the Array of LayerAnim on layers, using layer names or layer indexes, beginning at startTime
See LayerAnim object

parameters

layers | Layers where to paste the animation
layerAnims | Array of LayerAnim, default: Duik.copiedAnim
startTime | float, default: comp.time
useIndexes | boolean, true to use layer indexes instead of their names, default: Duik.settings.pasteAnimUseIndexes

returns

integer, number of layers on which animations were pasted
Duik.setup

Methods and attributes to correctly install libDuik & pseudo effects.

Duik.setup Attributes

Duik.setup.presetEffects

Name	Type	Description
presetEffects	string	The XML (as string object) to insert just before </effects> in After Effects presetEffects.xml to correctly install libDuik pseudo effects. / This includes the version of of libDuik as an XML comment, which can be checked by Duik.setup.checkPresetEffectsVersion to ensure libDuik has been correcly installed.

Duik.setup Methods

Duik.setup.installPseudoEffects()
Duik.setup.checkPresetEffectsVersion()

Name	Description	Return
installPseudoEffects()	Automatically install pseudo effects in After Effects presetEffects.xml	void
checkPresetEffectsVersion()	Checks the version of installed libDuik pseudo effects, stored in Duik.presetEffectsInstalledVersion	void

Duik.setup.installPseudoEffects()

Tries to Automatically install pseudo effects in After Effects presetEffects.xml.
The installation can be checked with Duik.checkPresetEffectsVersion(), en then comparing Duik.presetEffectsInstalledVersion with Duik.versionNumber.
Example:

//install
Duik.installPseudoEffects();

//check
Duik.checkPresetEffectsVersion();

if (Duik.presetEffectsInstalledVersion != Duik.versionNumber) {
//do something
} else {
//continue loading your script
}

parameters:

none

returns

void

Duik.setup.checkPresetEffectsVersion()

Checks the version of installed libDuik pseudo effects, stored in Duik.presetEffectsInstalledVersion.
See Duik.setup.installPseudoEffects() for an example.

parameters:

none

returns

void
Duik.uiStrings

Contains all string names used by effects created by Duik.
You can set these strings to translate libDuik at runtime.
Default values are English names.

Duik.uiStrings Attributes

Duik.uiStrings.ik
Duik.uiStrings.wiggle
Duik.uiStrings.exposure
Duik.uiStrings.rotMorph
Duik.uiStrings.swing
Duik.uiStrings.wheel
Duik.uiStrings.lensFlare
Duik.uiStrings.distanceLink
Duik.uiStrings.spring

Name	Type	Description
ik	string	"IK"
wiggle	string	"Wiggle"
exposure	string	"Exposure"
rotMorph	string	"Rotation Morph"
swing	string	"Swing"
wheel	string	"Wheel"
lensFlare	string	"Lens Flare"
distanceLink	string	"Distance Link"
spring	string	"Spring"

Duik.settings

Access to settings used by Duik.

Duik.settings Attributes

These attributes define some settings and preferences needed by Duik.
If you set them, they can be saved to be reloaded even if After Effects is shutdown, using Duik.settings.save(). If this method is not called, the settings will be set back to previous values if After Effects is shut down.
Saved settings must be loaded at runtime calling Duik.settings.load().
Default values can be restored using Duik.settings.restoreDefaults().

Duik.settings.controllerSize
Duik.settings.controllerSizeAuto
Duik.settings.controllerSizeHint
Duik.settings.boneType
Duik.settings.boneSize
Duik.settings.boneSizeAuto
Duik.settings.boneSizeHint
Duik.settings.boneColor
Duik.settings.morpherCreatesKeyframes
Duik.settings.pasteAnimUseIndexes

Name	Type	Description	Default
controllerSize	integer	Size of controllers in pixels	100
controllerSizeAuto	boolean	If true, controller sizes will be automatically adapted to comp size, according to Duik.settings.controllerSizeHint	true
controllerSizeHint	integer	Enumerated value, one of: / Duik.sizes.SMALL / Duik.sizes.MEDIUM / Duik.sizes.BIG	Duik.sizes.MEDIUM
boneType	integer	Enumerated value, one of: / Duik.layerTypes.NULL / Duik.layerTypes.SOLID	Duik.layerTypes.SOLID
boneSize	integer	Size of bones in pixels	20
boneSizeAuto	boolean	If true, bone sizes will be automatically adapted to comp size, according to Duik.settings.boneSizeHint	true
boneSizeHint	integer	Enumerated value, one of: / Duik.sizes.SMALL / Duik.sizes.MEDIUM / Duik.sizes.BIG	Duik.sizes.MEDIUM
boneColor	string	Hex value of the color of the bones, excluding leading « # »	« FF0000 »
morpherCreatesKeyframes	boolean	If true, morpher will automatically create keyframes for each keyframe of the controlled properties	True
pasteAnimUseIndexes	boolean	If true, Duik.pasteAnim will use layer indexes instead of their names by default. This can always be overriden with the parameters of the method	false

Duik.settings Methods

Duik.settings.save()
Duik.settings.load()
Duik.settings.restoreDefaults()

Name	Description	Return
save()	Saves Duik settings into After Effects preferences	void
load()	Loads Duik settings from After Effects preferences	void
restoreDefaults()	Restore default values to Duik settings	void

Duik.settings.save()

Saves Duik settings attributes into After Effects preferences (using app.settings.saveSetting())
Those settings can be loaded when the script runs using Duik.settings.load(). This allows to easily restore the settings set by the user even if After Effects is shut down.

parameters:

none

returns

void

Duik.settings.load()

Loads Duik settings attributes from After Effects preferences (using app.settings.getSetting())
This allows to easily restore the settings set by the user even if After Effects is shut down.
If this method is not called at runtime, default values will be loaded at first run.

parameters:

none

returns

void

Duik.settings.restoreDefaults()

Restore default values to Duik settings. These values will not be saved until Duik.settings.save() is called.

parameters:

none

returns

void

Duik.utils

Some useful methods.

Duik.utils Methods

Duik.utils.prepareProperty(property,isFX,index,depth,parentName)
Duik.utils.getPropertyDimensions(property)
Duik.utils.getLength(value1,value2)
Duik.utils.getAverageSpeed(layer,property)
Duik.utils.addPseudoEffect(layer,pseudoEffectName)
Duik.utils.getPuppetPins(effects)
Duik.utils.getDistance(layer1,layer2)
Duik.utils.rigProperty(layer,prop,pseudoEffect)
Duik.utils.deselectLayers()
Duik.utils.checkNames(comp)
Duik.utils.getItem(items, itemIndex)
Duik.utils.getKey(prop, keyIndex)
Duik.utils.getPropertyAnims(prop, selectedKeysOnly, startTime, endTime)
Duik.utils.getPropertyAnim(prop, selectedKeysOnly, startTime, endTime)
Duik.utils.setPropertyAnim(prop, propAnim, startTime)
Duik.utils.addKey(prop,key, startTime)
Duik.utils.getFirstKeyTime(prop)
Duik.utils.hasSelectedKeys(prop)
Duik.utils.convertCollectionToArray(collection)
Duik.utils.prepIK(layers)

Name	Description	Return
prepareProperty(property, isFX, index, depth, parentName)	Prepares property to be rigged	true if property can set expression, false otherwise
getPropertyDimensions(property )	Gets the dimensions of the property (1, 2 or 3), taking care of 2D layer positions (reported as 3D by AFX, but to be considdered as 2D)	integer, number of dimensions
getLength(value1, value2)	Gets the length between the values, whichever dimensions they are	float, length between the values
getAverageSpeed(layer, property)	Gets the average speed of the animated property, between its first and last keyframe only	float, average speed of the property
addPseudoEffect(layer, pseudoEffectName)	Adds a Duik predefined pseudo effect to the layer	Property, the effect added
getDistance(layer1,layer2)	Measure distance between two layers	integer, distance between layers, in pixels
getPuppetPins(effects)	Gets all puppet pins from a layer effects	Array of Properties, all puppet pins found
rigProperty(layer, prop, pseudoEffect)	Performs some checks on the property and adds a pseudo effect on the layer	Property, the effect added
deselectLayers()	Deselects all layers	Void
checkNames(comp)	Checks for duplicate names among the layers of the comp, renaming them if found.	true if any layer was renamed
getItem(items, itemIndex)	Gets the item as if it were in a 0-based indexed Array, even if it is in a 1-based indexed Collection	Object, the item
getKey(prop, keyIndex)	Gets the keyframe at keyIndex on the property	KeyFrame object
getPropertyAnims(prop, selectedKeysOnly, startTime, endTime)	Gets the keyframe animations on the child properties of the prop, if it's a PropertyGroup (recursive), or the animation of the prop if it's a Property	Array of PropertyAnim objects
getPropertyAnim(prop, selectedKeysOnly, startTime, endTime)	Gets the keyframe animation of the Property	PropertyAnim object
setPropertyAnim(prop, propAnim, startTime)	Sets the animation on the property	boolean, true if succeeded
addKey(prop,key, startTime)	Adds a keyframe on the property	void
getFirstKeyTime(prop)	Gets the time of the first key on the property	float, time of the keyframe
hasSelectedKeys(prop)	Checks if the properties has keyframes which are selected	Boolean
convertCollectionToArray(collection)	Converts the given Collection to an array. If the parameter is already an Array, returns a copy of it.	Array
prepIK(layers)	Creates an IKRig object, automatically detecting each layer usage.	IKRig object

Duik.utils.prepareProperty(property,isFX,index,depth,parentName)

Prepare the given property to be rigged.
isFX, index, depth, parentName will be filled by the method with the values corresponding to this property.

parameters:

property | Property
isFX | boolean
index | integer
depth | integer
parentName | string

returns

true if property can set expression, false otherwise

Duik.utils.getPropertyDimensions(property)

Gets the dimensions of the property (1, 2 or 3), taking care of 2D layer positions (reported as 3D by AFX, but to be considdered as 2D)

parameters:

property | Property

returns

integer, number of dimensions

Duik.utils.getLength(value1, value2)

Gets the length between the values, whichever dimensions they are

parameters:

value1 | float or Array of float, first coordinates
value1 | float or Array of float, second coordinates

returns

float, length between the values

Duik.utils.getAverageSpeed(layer, property)

Gets the average speed of the animated property, between its first and last keyframe only.

parameters:

layer | AVLayer of the property
property | Property

returns

float, average speed of the property

Duik.utils.addPseudoEffect(layer, pseudoEffectFileName)

Adds a Duik predefined pseudo effect to the layer. The AFX preset file of the pseudo effect must be located in the same folder as libDuik.jsxinc and called « Duik_ » + pseudoEffectName + « .ffx ».
In the preset, the effect must be called pseudoEffectName.

parameters:

layer | AVLayer
pseudoEffectFileName | string, name of the file of the pseudo effect

returns

Property, the effect added

Duik.utils.getPuppetPins(effects)

Recursive method to find all puppet pins on a given layer, even if there is more than one puppet effect. You must provide the effects PropertyGroup of the layer.
Example : var pins = Duik.utils.getPuppetPins(app.project.activeItem.layer(1)(« Effects »);

parameters:

effects | PropertyGroup, the effects group of a layer

returns

Array of Property, the puppet pins

Duik.utils.getDistance(layer1,layer2)

Measures distance between two layers, in pixels.

parameters:

layer1 | AVLayer
layer2 | AVLayer

returns

integer, distance in pixels

Duik.utils.rigProperty(layer, prop, pseudoEffect)

Performs some checks on the property and adds a pseudo effect on the layer.
The AFX preset file of the pseudo effect must be located in the same folder as libDuik.jsxinc and called « Duik_ » + pseudoEffectName + « .ffx ».
In the preset, the effect must be called pseudoEffectName.

parameters:

layer | AVLayer
prop | Property
pseudoEffect | file name of the pseudo effect

returns

PropertyGroup, the effect added

Duik.utils.deselectLayers()

Deselects all layers

returns

void

Duik.utils.checkNames(comp)

Checks for duplicate names among the layers of the comp, renaming them if found. This method is called everytime libDuik creates an effect which involves expressions and more than one layer, to avoid any bug with expressions linking to wrong layers.

parameters:

comp | CompItem where are the layers which must be checked. Default: app.project.activeItem

returns

true if any layer was renamed, false otherwise.

Duik.utils.getItem(items, itemIndex)

After effects sometimes uses its own Collection class, which is very similar to Arrays, but the first element of a Collection is at index 1 instead of 0 as in an Array.
This can make it difficult to write functions which will work both on Array or Collections.
Example:

function doSomethingOnLayers(layers) {
for (i = 0 ; i < layers.length ; i++) {
var layer = layers[i];
//do something
}
}

//will work correctly, as selectedLayers is an Array beginning at index 0
doSomethingOnLayers(app.project.activeItem.selectedLayers);

//will not work, as layers is a LayerCollection beginning at index 1
doSomethingOnLayers(app.project.activeItem.layers);

This method makes it possible to get an item both for an Array or a Collection, without knowing which type is given.

function doSomethingOnLayers(layers) {
for (i = 0 ; i < layers.length ; i++) {
var layer = Duik.utils.getItem(layers,i);
//do something
}
}

//both will work correctly
doSomethingOnLayers(app.project.activeItem.selectedLayers);
doSomethingOnLayers(app.project.activeItem.layers);

parameters:

items | Array or Collection
itemIndex | int, index where the item must be found

returns

Object, the item at itemIndex in items.

Duik.utils.getKey(prop, keyIndex)

Gets the keyframe at keyIndex on the property
see KeyFrame object

parameters:

prop | Property
keyIndex | int

returns

KeyFrame object

Duik.utils.getPropertyAnims(prop, selectedKeysOnly, startTime, endTime)

Gets the keyframe animations on the child properties of the prop, if it's a PropertyGroup (recursive), or the animation of the prop if it's a Property, beginning at startTime and ending at endTime.
This is a recursive method.
see PropertyAnim object

parameters:

prop | PropertyBase
selectedKeysOnly | boolean
startTime | float
endTime | float

returns

Array of PropertyAnim objects

Duik.utils.getPropertyAnim(prop, selectedKeysOnly, startTime, endTime)

Gets the keyframe animation of the Property
see PropertyAnim object

parameters:

prop | Property
selectedKeysOnly | boolean
startTime | float
endTime | float

returns

PropertyAnim object

Duik.utils.setPropertyAnim(prop, propAnim, startTime)

Sets the animation on the property, beginning at startTime
see PropertyAnim object

parameters:

prop | PropertyBase
propAnim | PropertyAnim object
startTime | float

returns

boolean, true if succeeded.

Duik.utils.addKey(prop,key, startTime)

Adds a keyframe on the property. You can offset the time by setting startTime
see KeyFrame object

parameters:

prop | PropertyBase
key | KeyFrame object
startTime | float, default: 0

returns

void

Duik.utils.getFirstKeyTime(prop)

Gets the time of the first key on the property.

parameters:

prop | Property

returns

float

Duik.utils.hasSelectedKeys(prop)

Checks if the properties has keyframes which are selected.

parameters:

prop | Property

returns

boolean

Duik.utils.convertCollectionToArray(collection)

Converts the given Collection to an array. If the parameter is already an Array, returns a copy of it.

parameters:

collection | Collection or Array

returns

Array

Duik.utils.prepIK(layers)

Creates an IKRig object, automatically detecting each layer usage.
The detection checks the hierarchy of the layers to find each layer usage.
If the detection fails, the IKRig object is created using the order of the layers in the Array or LayerCollection: the first are the layers, beginning by the last child, the last one is the controller.
Goal layers are detected by measuring the distance between the last child of the chain and the controller: goal layers and controllers should be at the same place.
See IKRig object.

parameters:

layers | Array of AVLayers or LayerCollection

returns

IKRig object